Understanding mmap and munmap:

The mmap system call in Linux serves the purpose of mapping files or devices into memory. It facilitates memory-mapped file I/O, enabling applications to access files on disk as part of their address space. Conversely, munmap is utilized to unmap an area previously mapped.

Syntax:
void *mmap(void *addr, size_t length, int prot, int flags, int fd, off_t offset);

`addr`: Starting address for the mapping; typically NULL, allowing the system to choose.
- `length`: Length of the mapping.
- `prot`: Desired memory protection
- `flags`: Determines the visibility of updates to the mapping (`MAP_PRIVATE` for a private copy-on-write mapping, `MAP_SHARED` for a shared mapping).
- `fd`: File descriptor of the file to be mapped.
- `offset`: Offset in the file/device where the mapping should start.

munmap Syntax:
int munmap(void *addr, size_t length);
- `addr`: Address of the mapping.
- `length`: Length of the mapping.

Code:

Initial Program Setup (first.c)
- VmPeak: Displays the peak virtual memory size used by the process throughout its lifetime.
- VmSize: Represents the current virtual memory size of the process, indicating the total amount of virtual memory allocated by the process.
- VmRSS: Denotes Resident Set Size, i.e., the amount of physical memory currently utilized by the process.

This stage shows the baseline memory usage of the program without any modifications, offering an insight into how much memory a simple allocation and initialization of an array impacts the virtual and physical memory sizes.

Execution steps:
gcc -Wall -o prvi first.c
./prvi

After Adding Memory Mapping (second.c)

Memory Mapping (mmap):
- An anonymous memory page is requested from the operating system, not backed by any file, and is set to be private, meaning it won't be shared with other processes.

Virtual Memory (VmSize):
- After memory mapping using mmap, VmSize increases by at least the size of one memory page. This reflects the allocation of virtual memory space which initially does not require physical memory backing (not visible in VmRSS until accessed).

This step allows observation of the effect of memory mapping on virtual memory size without yet affecting physical memory, demonstrating how mmap allocates address space.

Execution steps:
gcc -Wall -o drugi second.c
./drugi

After Writing Data to Mapped Memory (third.c)

Writing Data:
- The program writes data into the memory-mapped page. This is typically done to trigger the allocation of physical memory as the operating system must now back the previously virtual-only page with actual RAM.

Physical Memory Usage (VmRSS):
- Following the data write into the memory-mapped page, VmRSS increases. This change occurs because the OS needs to allocate a physical page to store the data written, hence increasing the actual RAM usage.

This final step demonstrates the demand paging mechanism where physical memory allocation is deferred until a page is actually written to. It provides a practical example of how VmRSS can be used to track physical memory usage changes in response to program actions.

Execution steps:
gcc -Wall -o treci third.c
./treci

Throughout these stages, we can observe how virtual and physical memory management play roles in application performance and resource usage. Mmap provides a flexible way to manage memory, optimizing usage by delaying physical allocation until necessary, thereby efficiently managing system resources. This approach is crucial for applications requiring large amounts of memory or for systems where memory usage efficiency is critical.